## Slide 1: MUTUAL AUTHENTICATION IN IoT SYSTEMS USING PUF
P.HEMALATHA [1418114]
S.MANJU [1418125]
M.NANDHINI [1418129]
V.VINOTHA [1418153]

## Slide 2: PROBLEM IDENTIFICATION
OTP
Group authentication protocol
Certificate based authentication protocol
Physical unclonable functions
Trusted third party and ZKPK

## Slide 3: Solution
Our proposed PUF maps a set of challenges to a set of responses based on intractably complex physical system.
R= P(C)
R is the response of a PUF
C is the challenge given to the PUF
Challenge C and its response R from a PUF is called a challenge response pair.
Our proposed PUF can be used to perform authentication between a user and a server as well as used to perform authentication between two IoT devices.

## Slide 4
When an IOT device is deployed in the field for the first time, an operator inputs a password into the device to exchange the initial CRP with the server using the TOTP approach.
Once the initial CRP is exchanged with the server, the IOT device can function independently without the need for any operator.
Thus, the server stores the identity IDA, and the CRP(Ci,Ri) for each IOT device, while the IOT device does not store anything.

## Slide 5: Design Classification
Mutual authentication of IoT device and server
Mutual authentication of two IoT devices

## Slide 6: Mutual authentication of IoT device and server
MODULE 1
Input: IDA,N1
Process:
Find IDA in Memory
Read CRP(Ci,Ri)
Generate RS1
Ma={IDA,N1,Rs1}Ri
Output: Ci,MA,MAC(Ma||Ri||Rs1)

## Slide 7: Module 2
Input: Ci,Ma,MAC(Ma||Ri||Rs1)
Process:
Ri=PA(Ci)
Obtain Rsi using Ri and verify MAC
Generate NA
Ci+1=H(Na||Rs1)
Ri+1=PA(Ci+1)
Ms={Ida,NA,Rs1,Ri+1}Ri
Output: Ms,MAC(Ms||Ri||Na)

## Slide 8: Module 3:
Input: Ms,MAC(Ms||Ri||Na)
Process:
Obtain NA and Ri+1 using Ri
verify MAC
Ci+1=H(NA||Rs1)
Output:
Server rejects the authentication or two entities can now form a session

## Slide 9: Flow Diagram
IoT device IDA
Server IDs
1
2
3
Ida,N1
Ci,Ma,MAC(Ma||Ri||Rs1)
Ms,MAC(Ms||Ri||Na)

## Slide 10: Mutual authentication of two IOT devices
MODULE 1 :
Input : IDA,IDB,N1,N2
Process : find IDA,IDB in memory
read tha CRPs(Ci,Ri),(Cj,Rj)
generate RS1,RS2
MB={IDA,IDB,N2,RS1,RS2}Ri
MA={IDA,IDB,N1,RS1,RS2,MB}Ri
Output : Ci,Cj,MA,MAC(IDA,MA||Ri||RS1),MAC(IDB,MB||Rj||RS2)

## Slide 11: Module 2
Input : Ci,Cj,MA,MAC(IDA,MA||Ri||RS1),MAC(IDB,MB||Rj||RS2)
Process : Ri=PA(Cj)
obtain RS1,RS2 and MB using Ri
verify MAC
generate :NA and NB
Ci+1=H(NA||RS1)
Ri+1=PA(Cj+1)
MS1={IDA,NA,RS1,Ri+1}Ri
MB1={IDA,NB}RS2
Output : IDA,MS1,MAC(MS1||Ri||NA)

## Slide 12: Module 3
Input : IDA,MS1,MAC(MS1||Ri||NA)
Process : obtain NA and Ri+1 using Ri
verify MAC
Ci+1=H(NA||RS1)
Output : Cj,MB,MB1,MAC(MB||Rj||RS2),MAC(MB1||RS2||NB)

## Slide 13: Module 4
Input : Cj,MB,MB1,MAC(MB||Rj||RS2),MAC(MB1||RS2||NB)
Process : Rj=PB(Cj)
Obtain RS1 and RS2 using Rj
Obtain NB using RS2
Verify MACs
Generate NB
Cj+1=H(NB||RS2)
Rj+1=PB(Cj+1)
MS2={IDB,NB,RS2,Rj+1}Rj
Output : IDB,MS2,MAC(MS2||Rj||NB)

## Slide 14: Module 5
Input : IDB,MS2,MAC(MS2||Rj||NB)
Process :Obtain NB and Rj+1 using Rj
Verify MAC
Cj+1=H(NB||RS2)
Output : MAC(IDA||IDB||N3||RS1)

## Slide 15: Flow diagram
IoT Device IDA
Server IDs
IoT Device IDB
1
2
3
4
5
6
7
IDA,N1
IDB,N2
Ci,Cj,MA,MAC(IDA,MA||Ri||RS1),MAC(IDB,MB||Rj||RS2)
IDA,MS1,MAC(MS1||Ri||NA)
Cj,MB,MB1,MAC(MB||Rj||RS2),MAC(MB1||RS2||NB)
IDB,MS2,MAC(MS2||Rj||NB)
MAC(IDA||IDB||N3||RS1)

## Slide 16: Thank you